## Slide 1
Design of Local Resonance Units for Tollmien-Schlichting Waves Attenuation
Author: Vivek Kande
Supervisors: Dr. ir. Theodoros Michelis
Pierre Champeaux
30th September 2026

## Slide 2
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 3: Motivation
Aviation contributes to 5% global radiative forcing which is expected to more than double by 2050
Increasing Aircraft efficiency through aerodynamic improvements
Ricco et al. [1]
Notes: Climate impact
Aerodynamic way
Drag reduction
Visoucs drag fuel
Fundamental approach
How does drag
Boundary layer

## Slide 4: Boundary layer transition
External disturbances
perturbation
mean
External disturbances translate to flow instabilities that evolve and trigger transition.
Avallone et.al [2]
Kachanov [3]
Notes: 1) Gradient
Laminar to turbulent
Transition delay
How transition occurs (don’t mention waves)
2) If we decompose the flow field into—
Q=uvp
3) Linear region small amplitude

## Slide 5: Linear stability
External disturbances
Within the linear region they exhibit a certain relation the growth rate is a function of the frequency and streamwise location
Growth rate =
Wavenumber =
Frequency=
Complex Wavenumber
Ansatz:
+
-
+
-
+
-
+
-
+
Unstable region
Streamwise location
Amplitude metric
Kachanov [3]
Champeaux [4]
Notes: Detailed look at linear region
Example instability (wall normal perturbation)-looks like a wave – harmonic nature
we can model this with a complex wave ansatz
Boundary layer- drag
Transition phenomena
Linear regime
Example wave
Complex ansatz
Evolution
Transition delay

## Slide 6: TS waves
2D waves with unique eigen functions/ shape functions
Unique relation between the perturbation quantities governed by the Navier stokes equation
Wall admittance
Notes: One way to access or view this relation is through the lens of admittance

## Slide 7: Flow control
Base flow modification
Direct wave control
Active
Passive
Control element
Controlled actuation
Controlled response
T.F
TS wave actuation
response
Notes: It can be something like a plasma actuator or something very rudimentary like an oscillating plate driven by a motor
TF-Inherent dynamics of the system
4
 Need for passive flow control

## Slide 8: Wave interference mechanism
Input TS wave
C.E.
+
Wall admittance
Representative image →wave interference
Amplitude 
Phase 
Attenuation or amplification 
Notes: As mentioned earlier we operate entirely in the linear regime, hence classical wave phenomena superposition or interference
And an admittance maps would give us this relation

## Slide 9: Surface admittance characterization
Design requirement #1:
Favorable admittance phase:
Amplitude 
Phase 
Attenuation or amplification 
Admittance map
Champeaux [4]
Input TS wave
act
act
Input B.C
Output flow
Notes: We are establishing a design requirement

## Slide 10: Passive control methods examples #1
TS wave excitation
Internal dynamics: Periodic oscillations of airflow
Wall admittance modification
TS wave modulation:
Wave interference
The control element and the boundary layer have matching inertial properties: admittance matching
Maximum energy transfer The perturbation velocities and the response velocities are of comparable magnitudes
Porous wall
Rouviere et al. [5]
Notes: an example of a passive flow control with admittance modification
Mechanism, inherent transfer function
Additionally admittance matching max energy
Recirculation region focus on solid based

## Slide 11: Compliant wall
TS wave excitation
Internal dynamics: surface waves of compliant walls
Wall admittance modification
TS wave modulation:
Wave interference
The control element and the boundary layer have significantly different inertial properties: admittance mismatch
Low energy transfer: The response velocities significantly smaller than that of the input TS wave in air
Passive control methods example
Carpenter[6]

## Slide 12: The resonance advantage
Using resonance to overcome the admittance matching limitation
The natural phase variation of resonant systems mean that one can selectively tune the system with respect to the frequency of the TS wave to operate the right phase.
Maximum energy transfer at resonance frequency
Design requirement #1:
Favorable admittance phase: close to resonance
Notes: When you excite the system close to its natural frequency you have maximum energy transfer and hence max admittance amp.

## Slide 13: Scale separation (local resonance)
Pressure perturbation
In a local resonance unit (LRU): by operating at a subwavelength scale (local interaction) we avoid imposition of scales of TS wave on the resonator while still imposing a near uniform admittance phase
Pressure load
Representative image of periodic array of LRUs
This local resonance condition is a premise for metamaterial application in multiple fields, where a periodic array of LRUs is implemented
Design requirement #2:
Must be tuned to operate at a subwavelength scale

## Slide 14
Helmholtz resonator
Local resonance concepts explored till now
Helmholtz resonator
Phononic subsurface
Spring mass system
Phononic subsurface
Michelis et al.[7]
Hussein et al.[9]
Michelis et al.[8]
Notes: Some of the resonance concepts explored till now.
Need to explore alternate

## Slide 15: Recap and Problem definition
TS wave excitation
Internal dynamics: wall normal oscillations
Wall admittance modification
TS wave modulation:
Wave interference
Amplitude 
Phase 
Attenuation or amplification 
Admittance map
Design requirement #1:
Favorable admittance phase: close to resonance
Design requirement #2:
Must be tuned to operate at a subwavelength scale
Design requirement #3:
Tuned to follow #1,#2 at TS wave frequency
Hypothetical
system
Notes: Lack of research on concepts following #1 or the inability of the existing concepts to follow #1 brings us to the current work

## Slide 16: Alternative LRU concepts explored
Single mass composite resonator (SMCR)
Double mass composite resonator (SMCR)
Notes: Lack of research on such
Although just like a simple spring mass system we don’t know if we can tune it, we also don’t know how the phase varies across different modes
Playing with phase shifts

## Slide 17
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 18: Research objective and questions (simplified)
Investigating the potential of composite resonators as LRU concepts designing them to achieve surface admittance suitable for TS wave attenuation as per the design criteria.
  How does the admittance phase of composite resonators vary across different resonance modes and how can we tune it?
  How can they be tuned to operate at a desired frequency while maintaining subwavelength dimensions?
  How much TS wave attenuation do the tuned designs result in?
Stage I
Conceptual exploration of admittance phase
Stage II
LRU Tuning
Stage III
TS wave interaction

## Slide 19
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 20: Methodology
Pressure load analysis: Linear elastic modelling in COMSOL
TS wave interaction: Harmonic Navier Stokes (HNS) equations solver
H
LRU
TS wave
L
Notes: Most part pressure load analysis
Uniform pressure load since the LRU is expected to see only a small part of the TS wave
Top shows BC
And the bottom shows problem schematic

## Slide 21: Scale separation limit
H
LRU
TS wave
Act
Design requirement #2:
Must be tuned to operate at a subwavelength scale
Velocity at the wall is assigned independent of local pressure
Scale separation implies that the TS waves must be indifferent to local variations
Type-A
Const. phase
Type-B
Linearly growing phase
Average velocity phase is same in both cases
L
Notes: The requirement #2 doesn’t have the exact limit
We move to an active system to set the design requirement since we want some freedom in controlling the response
We test scale separation by examining one of its fundamental traits

## Slide 22: Scale separation limit
Modulation of TS wave amplitude measured downstream
Width of actuator
H
LRU
TS wave
Act
Design requirement #2:
Must be tuned to operate at a subwavelength scale
act
act
Notes: The graph on right shows change in n factor at x1
x axis shows width of actuator
The ts wave must not be able to tell the difference between type a and type b.

## Slide 23
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 24: Objectives
  To examine admittance phase variation across different vibration modes of SMCR and DMCR.
  To determine how to tune them to obtain the desired admittance phase close to resonance.
24
Notes: Exmaine modes
See if we can tune them

## Slide 25: SMCR-numerical investigation
Fixed sides
Rigid element
Soft element
25
Favorable phase region or Stable region
Notes: different mode shapes (non uniform admittance phase at higher modes)
we see favorable phase only in a narrow region between rm-1 and arm -1
we disregard higher modes (low amp, high freq)

## Slide 26: Primary Mode
26
Helmholtz resonator
Michelis et al.[7]
Hussein et al.[9]
Michelis et al.[8]
Notes: Looks exactly the same as previous concepts

## Slide 27: DMCR-numerical investigation
Rigid elements
Soft element
2
2
Fixed sides
27
Notes: Additional peak, different mode response
They oscillate out of phase with each other

## Slide 28: DMCR- Coupled resonance
Increasing
1
2
3
4
28
Notes: As they move close to each other we lose the favorable phase region between the resonance peaks
And the same story as they move further closer where we see the coupled resonance
And finally we see a single broad peak
So the addition of a mass or a degree of freedom did not give any advantage in realizing the favorable admittance phase close to resonance

## Slide 29: Energy Transfer analysis
LRU
Work done on the LRU
Conclusion: Any passive linear LRU with single input single output (SISO)architecture are limited to a certain admittance phases achievable.
29
Hypothetical
system
Notes: Now We don’t know If we can tune these systems by changing shapes sizies or materials to affect the phase
But there is a fundamental issue limiting the admittance phase
That is understood by energy transfer analysis
- concusion on siso
This means this dream system is ahceivable oonly through energy inputs
In real systems this means that we are limited to post resonance conditions

## Slide 30
Design phase points
Design requirement #1:
Favorable admittance phase: close to resonance
Design requirement #2:
Must be tuned to operate at a subwavelength scale
Design requirement #3:
Tuned to follow #1,#2 at TS wave frequency
SMCR systems
DMCR systems
Design phase point
Design requirement #1:
Favorable admittance phase: close to resonance
30
Notes: For the next stage we would focus on tuning the design phase point to have the desired frequency

## Slide 31
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 32: Objectives
  To tune the composite resonators such that they follow the subwavelength requirement and their design phase point is at TS wave frequency.
  Additionally tune them to increase the admittance amplitude
32

## Slide 33: 1D-Analytical modelling
Design phase point
Analytical parametric studies conducted to guide the numerical parametric studies
Notes: We take an analytical approach
As you can see the admittance obtained from analytical sdof model and the smcr in comsol show a good match

## Slide 34: Analytical investigation
Design phase point amplitude
Design phase point frequency
To increase the amplitude, one cannot rely on stiffness or mass alone
34
Design phase point

## Slide 35: Role of material constraints
Ashby[9]
Notes: To keep high amplitudes we want to explore different material choices

## Slide 36: Tuned design admittance
Design requirement #2:
Must be tuned to operate at a subwavelength scale
Design requirement #3:
Tuned to follow #1,#2 at TS wave frequency
Design requirement #1:
Favorable admittance phase: close to resonance
Soft element
Rigid element
Fixed sides
Notes: Tuned design that meets all the design criteria

## Slide 37: DMCR-numerical investigation
The amplitude achievable is limited again by the density and stiffness constraints together.
Frequency of design phase point -3
Admittance amplitude of design phase point -3
Notes: Red line shows parameter space with the design phase point’s frequency being the ts wave frequency

## Slide 38: Tuned design admittance
Design requirement #2:
Must be tuned to operate at a subwavelength scale
Design requirement #3:
Tuned to follow #1,#2 at TS wave frequency
Design requirement #1:
Favorable admittance phase: close to resonance
Design phase point
The coupled resonance phenomena doesn’t give us an amplitude advantage either
Fixed side
Fixed side
Soft element
rigid element-2
rigid element-1
Notes: Dmcr gave neither the phase advantage nor the amplitude advantage

## Slide 39
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 40: Objectives
  To find the order of TS wave attenuation achievable from the composite resonators
40

## Slide 41: TS wave attenuation from SMCR
H
LRU
TS wave
Spatial variation of admittance
Streamwise location

## Slide 42: TS wave attenuation from DMCR
H
LRU
TS wave

## Slide 43
Background and research gap
Research questions
Methodology
Stage-I
Stage-II
Stage-III
Conclusions

## Slide 44: Answers to the research questions
  How does the admittance phase of composite resonators vary across different resonance modes and how can we tune it?
  How can they be tuned to operate at a desired frequency while maintaining subwavelength dimensions?
  How much TS wave attenuation do the tuned designs result in?
The admittance phase is outside the favorable limits except for a narrow range of post resonance frequencies
Passivity limits the admittance phase values of SISO systems
No advantage from coupled resonance
to (for air based boundary layer)
The exact subwavelength limit was identified through scale separation test
Tuning workflow is provided to meet the operating conditions

## Slide 45: Recommendations
For a water based boundary layer the SMCR based LRUs can be further explored for optimization and practical implementation.
Although the attenuation of a single composite resonator based LRU is low, one can achieve cumulative attenuation through implementation in aperiodic array.
Considering the limitation of SISO type systems in admittance phase, multiple input multiple output (MIMO) type systems can be explored.
Further verification in fully coupled fluid structure interaction simulations.
TS wave
LRU
LRU
Notes: water

## Slide 46: References
[1]. P. Ricco, M. Skote, and M. A. Leschziner, “A review of turbulent skin-friction drag reduction by near-wall transverse forcing,” en, Progress in Aerospace Sciences, vol. 123, p. 100713, May 2021, ISSN: 03760421. DOI: 10.1016/j.paerosci.2021.100713.
[2] F. Avallone et al., Metamaterials and Fluid Flows, en, arXiv:2509.05371 [cond-mat], Sep. 2025. DOI: 10.48550/arXiv.2509.05371. Accessed: Jan. 12, 2026. [Online]. Available: http://arxiv. org/abs/2509.05371.
[3] Y. S. Kachanov, “Physical mechanisms of laminar-boundary-layer transition,” Annual review of fluid mechanics, vol. 26, no. 1, pp. 411–482, 1994.
[4] P. Champeaux, “Towards direct wave control of Tollmien–Schlichting instability,” en, Tech. Rep.
[5] A. Rouviere, F. Méry, J. Methel, O. Vermeersch, and M. Forte, “Experimental and Numerical Study on Wall Impedance Effects on Tollmien–Schlichting Waves,” en, AIAA Journal, pp. 1–12, Sep. 2021, ISSN: 0001-1452, 1533-385X. DOI: 10.2514/1.J060536. Accessed: Dec. 8, 2025. [Online]. Available: https://arc.aiaa.org/doi/10.2514/1.J060536.
[6] P. W. Carpenter, “Current status of the use of wall compliance for laminar-øow control,” en, 1997.
[7] T. Michelis, C. De Koning, and M. Kotsonis, “On the interaction of Tollmien–Schlichting waves with a wall-embedded Helmholtz resonator,” en, Physics of Fluids, vol. 35, no. 3, p. 034104, Mar. 2023, ISSN: 1070-6631, 1089-7666. DOI: 10.1063/5.0141685. Accessed: Dec. 8, 2025. [Online]. Available: https://pubs.aip.org/pof/article/35/3/034104/2882036/On-the interaction-of-Tollmien-Schlichting-waves.
[8] M.I. Hussein, S. Biringen, O. R. Bilal, and A. Kucala, “Flow stabilization by subsurface phonons,” en, ProceedingsoftheRoyalSocietyA:Mathematical,PhysicalandEngineeringSciences,vol.471, no. 2177, p. 20140928, May 2015, ISSN: 1364-5021, 1471-2946. DOI: 10.1098/rspa.2014. 0928. Accessed: Dec. 8, 2025. [Online]. Available: https://royalsocietypublishing.org/ doi/10.1098/rspa.2014.0928.
[9] T. Michelis, A. B. Putranto, and M. Kotsonis, “Attenuation of Tollmien–Schlichting waves using resonating surface-embedded phononic crystals,” en, Physics of Fluids, vol. 35, no. 4, p. 044101, Apr. 2023, ISSN: 1070-6631, 1089-7666. DOI: 10.1063/5.0146795. Accessed: Dec. 8, 2025. [Online]. Available: https://pubs.aip.org/pof/article/35/4/044101/2883065/Attenuatio n-of-Tollmien-Schlichting-waves-using.

## Slide 47
Questions?

## Slide 48
Backup slides

## Slide 49: Wave interference mechanism (plots from results)
Baseline/ original TS wave
Additional wave resulting from admittance modification
Final modulated TS wave
Location of control element

## Slide 50: SMCR-numerical investigation
Soft element
Rigid mass
Fixed sides
Increase in “m”
Increase in “k”
(more than “m”)
Increase in “m” and “k”
Rigid mass density
Rigid mass width
SMCR thickness
Notes: Note the change in schematic of the smcr but the architcherutre remains same with rigid and soft

## Slide 51: Compliant wall
TS wave excitation
Internal dynamics: surface waves of compliant walls
Wall admittance modification
TS wave modulation:
Wave interference
The control element and the boundary layer have significantly different inertial properties: admittance mismatch
Low energy transfer: The response velocities significantly smaller than that of the input TS wave in air
Passive control methods examples #2

## Slide 52: Energy Transfer analysis
LRU
Work done on the LRU
Conclusion: Any passive linear LRU with single input single output (SISO)architecture are limited to a certain admittance phases achievable.
52